## Slide 1
Air Quality Modeling at EPA – Global to Urban scales
Jonathan E. Pleim & AQ Model Development Team
Office of Research and Development
USEPA
MUSICA Kick-off Meeting, May 21 – 22, 2019

## Slide 2
Atmospheric model development at EPA
Community Multiscale Air Quality (CMAQ) model is a comprehensive chemical transport model:
  gas, aerosol, aqueous chemistry
  photolysis including cloud and aerosol effects
  precipitation scavenging/wet deposition and convective cloud transport
  dry deposition and bidirectional surface flux
  dust, sea salt and biogenic emissions processes
WRF
  EPA added physics: ACM2, PX LSM, modified KF
WRF-CMAQ
  Two-way coupled w/ direct aerosol radiative feedback
MPAS
  EPA added physics: ACM2, PX LSM, modified KF
  Analysis FDDA
MPAS-CMAQ
  Two –way coupled on MPAS mesh

## Slide 3
CMAQv5.3
Highlights of new version to be released in June 2019
  Chemistry mechanisms updated and consolidated. Complexity of chemical speciation
    reduced
  Photolysis and halogen updates - long-range transport of ozone
  Expanded cloud aqueous chemistry including SOA production
  Biogenic secondary organic aerosol production revised
  Water uptake to aerosol organic phase – applications to
    chemistry, mixing state, optics, etc.
  Updates dry deposition of gases and aerosols
  Improved bidirectional surface flux for NH3

## Slide 4: Aerosols: Organic Aerosol in CMAQv5.3 (AERO7)
BIOGENIC EMISSIONS
isoprene
sesquiterpenes
benzene
low-yield aromatics
high-yield aromatics
ANTHROPOGENIC EMISSIONS
SV_ISO1 SV_ISO2
SVSQT
SVAVB3
AAVB3
AAVB4
ASQT
AISO1 AISO2
AORGC
AOLGA
AOLGB
POA
VOCs
GLY MGLY
cloud
water
EMISSIONS
EMISSIONS
EMISSIONS
pcSOA
IEPOX
AISO3
aqueous aerosol
+OH, + NO3
+ OH/NO
+ OH/NO
+ OH/NO
+OH, +O3, +NO3, +O3P
AGLY
SVAVB4
long
alkanes
SVAVB2
AAVB2
AAVB1
SVAVB1
PAHs
+ OH
OOA
OOG
POG
+OH
POC+NCOM
APIN monoterpenes
+OH, +O3, +O3P
TERP monoterpenes
+OH, +O3, +O3P
MTNO3
AMTNO3
AMTHYD
+NO3
SVMT1, SVMT2
SVMT3, SVMT4
SVMT5, SVMT6
AMT1, AMT2
AMT3, AMT4
AMT5, AMT6
pcSOG
+ OH
pcVOC
+ OH/NO
+ OH/HO2
AORGH2O
RH
Notes: Figure: Schematic of SOA in updated simulation. See Pye et al. 2017 for a description of the traditional and aqueous aerosol SOA systems. See Pye et al. 2015 for MTNO3 formation and hydrolysis. See Murphy et al. 2017 for a description of the semivolatile POA (POA, POG), oxidized POA vapors (OOA, OOG) and potential SOA from combustion sources (pcSOA) system. Species different from the default configuration are in red.
Improved consistency between SAPRC and CB SOA mechanisms
  Monoterpene organic nitrate SOA from SAPRC07tic (Pye et al. 2015 ES&T) now available in CB6r3-aero7.
  Included in aero6i and aero7i as well.
Reduced number of species required for primarily anthropogenic SOA (benzene, toluene, xylene, alkanes, PAHs/naphthalene) (all aero7/7i mechanisms)
Updated monoterpene photooxidation SOA (all aero7/7i mechanisms)
Uptake of water onto hydrophilic organics (all aero7/7i mechanisms)
Process analysis can now access contributions from individual aerosol microphysical processes (e.g. coagulation from Aitken to Accumulation mode, condensation to each mode, new particle formation, etc)

## Slide 5
NH3 Bidirectional surface flux
New NH3 bidirectional flux in CMAQ is closely linked to EPIC agriculture model
The bidi model uses daily inputs from EPIC for soil ammonia content, soil pH, soil moisture CEC, porosity, and wilting point to calculate Gg and cg
CMAQ
NH3(ppb)
CrIS
ca
Ra
0.5Rinc
Rbg
Rst
Rw
cc
cg
cst
Rsoil
Rb
Rb
0.5Rinc
Schematic of bidi model
Monthly average NH3 (ppb)
vs AMoN observations
June average NH3 concentrations
Vs CrIS retrievals
Pleim et al 2019, JAMES submitted

## Slide 6
Model evaluation
EPA models are used for policy development and air quality regulation as well as research
  Must have scientific review and credibility (journal articles, peer reviews)
  Every new version is rigorously evaluated
Max 8-hr O3
Max 8-hr O3
PM2.5
PM2.5
CMAQv5.3 Mean bias
May – August, 2016

## Slide 7
Drivers for global multiscale system
As AQ is cleaner in US, more comes from beyond our borders
  Current systems either rely on different global models for LBCs for regional AQ modeling or Multiple nesting from Hemispheric to regional and urban:
  Multi-step process, Many opportunities for user mistakes, Interpolation errors on boundaries, Resolution discontinuities, Map projection differences, No upscale feedback
DX = 108 km
DX = 12 km
DX = 1 km
DX = 4 km

## Slide 8
MPAS
MPAS with its capability for seamless refinement is ideally suited for global to local scale AQ modeling
MPAS uniform mesh (240 km)
MPAS non-uniform mesh (92km – 25km)
Refinement over CONUS

## Slide 9
MPAS-CMAQ
Integrated meteorology and chemistry on global domain with seamless refinement to local scales
  Simple efficient interface
    Call CMAQ as module similar to WRF physics
    Two-way interaction including aerosol feedbacks
  Transport (adv, diffusion) of chemical species in MPAS
    Ensure mass conservation
    Consistency with met parameters
    Minimize numerical diffusion and dispersion
Three configurations of flexible systems:
  Online global variable grid: MPAS-CMAQ)
  Online regional (WRF-CMAQ and limited area MPAS-CMAQ)
  Offline regional (WRF + CMAQ)
Uses latest version of CMAQ from public EPA Git Repo (no changes needed)
Future coupling to other met models (FV3)
MPAS

## Slide 10
Testing EPA mods to MPAS
July 2013
2-m Temperature Daily RMSE for CONUS

## Slide 11
MPAS w/ EPA physics & FDDA
July 2016 with 46km/12 km mesh resolution
EPA Physics – ACM2, PX LSM, modified KF
FDDA using 6-hrly GFS analyses at 0.25 deg resolution
Surface analyses for PX LSM soil nudging : 0.25-deg GFS with 12 km NAM blending over US
RMSE T-2m
RMSE WS-10m

## Slide 12
Initial testing of MPAS-CMAQ
Max 8hr Ozone – July 11 – 31, 2013
TOAR dataset includes ozone observations from many networks across the globe
Need more data for Asia (particularly China) and Africa
Observed
MPAS Simulated

## Slide 13
Conclusions
EPA AQ models are developed for policy development and regulatory planning as well as for air quality research
AQ models need to address issues relevant to implementation of policy goals:
  Improved capabilities for addressing local nonattainment issues
  Enable examination of US air pollution in context of changing global emissions
  Quantifying natural vs anthropogenic contributions
  Improved cross-media application capability
  Models must be state-of-the-science to withstand legal challenge
Expanding to global scale through coupling with MPAS is next step for serving both EPA’s mission and the research community
AMS 100the annual meeting session: Global to Local Scale Coupled Meteorology and Atmospheric Chemistry Modeling

## Slide 14
Disclaimer
The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the U.S. EPA

## Slide 15: New research on mechanistic approaches to monoterpene SOA formation
Changes in monoterpene SOA due to the NOx-oxidant-autoxidation couplings potentially responsible for a quarter of the recent downward trend in organic aerosol in the southeastern United States (Pye et al. 2019 PNAS)
Monoterpene oxidation products (ELVOC) are the dominant source of new particle number except where ammonia (NH3) or amines (e.g. DMA) are abundant (Murphy et al. in prep)
Predicted decline in HOM peroxy radical production in Atlanta, GA and other sites
New particle formation rates by pathway (May-June)
Monoterpene oxidation products dictate PM2.5 and new particle formation
Notes: HOM peroxy radical is proxy for MT SOA production

## Slide 16: Volatile chemical products important for urban air quality
CalNex 2010 CMAQ Modeling (Qin et al. in prep) Pasadena site
Background corrected SOA
Ozone
OH Reactivity
Modeling experiment to show that inclusion of more VOCs from VCPs improves SOA, ozone, and OH reactivity