## Slide 1: Updating Chemical Mechanisms in Models (e.g., CESM)
Becky Schwantes
July 30, 2018
GEOS-Chem / NCAR Models Workshop

## Slide 2
Current Tropospheric Chemical Mechanisms in CESM
Configuration / Compset | Model Top | Chemical Mechanism | Chemical Description
CAM-Chem | 40 km | TS1 | Troposphere and stratosphere
WACCM | 150 km | TSMLT1 | Troposphere, stratosphere, mesosphere, and lower thermosphere chemistry
TS1/TSMLT1 is an updated version of the MOZART-4 mechanism described in Emmons et al. 2010
  Speciated aromatics
  Updated isoprene and terpenes oxidation
  More speciated organic nitrates for improve comparison between models and observations
  Updated JPL rate constants (2015, No. 18)
  Gas-phase isoprene and terpene organic nitrate uptake to aerosols as done in GEOS-Chem described in Fisher et al. 2016.

## Slide 3: TS1 Chemistry Degree of Simplification
Base: 187 Transported species
34 Non-transported species
528 Reactions

## Slide 4: Future Development
Future Updates to TS1 / TSMLT1 Chemical Mechanism:
  Isoprene and terpene chemistry
  More speciation of alkane chemistry
  Improved halogen chemistry
  Improved chemistry related to precursors from fires (in coordination with upcoming campaigns)
  Tagged NOx Scheme
  Nitrate Aerosol Scheme - MOSAIC (Model for Simulating Aerosol Interactions and Chemistry) is being coupled with MAM4 in the CAM model (University of Wyoming, PNNL).
Notes: Rearrange this structure of this

## Slide 5: Upcoming Updates to Isoprene and Terpene Oxidation
Isoprene (NO3, O3, + OH)
Terpene (NO3, O3, + OH)
+ 13 Non-transported Species
+ 21 Transported Species
+ 117 Reactions
+ ~12% time to run
+ 19 Non-transported Species
+ 15 Transported Species
+ 101 Reactions
+ ~14% time to run
Isoprene + OH
Terpene + OH
Base: 187 Transported species
34 Non-transported species
528 Reactions

## Slide 6: Adding Gas-Phase Chemistry
  We have recently created a CAM-Chem wiki to explain how to run CAM-Chem including detailed descriptions of how to update chemistry
  Updating/adding gas-phase chemistry is relatively easy in CESM
  As discussed earlier today, future updates (e.g., Chem Café, MICM) will make this process even easier.
https://wiki.ucar.edu/display/camchem/Home

## Slide 7: Very Simplified Schematic of Chemistry in CESM
CLM (Community Land Model)
Biogenic Emissions
Dry-deposition
CAM (Community Atmosphere Model)
hv
O3
OH
Aerosols
NOx
Wet-deposition
To incorporate gas-phase chemistry:
Chemical processing
Photolysis
Wet/dry deposition
Aerosol uptake
Emissions

## Slide 8
  Convert your chemical mechanism to an input file (ASCII) that the CESM chemical preprocessor can read.
Solution
ALKNIT -> C5H11ONO2,
Not-Transported
ALKO2,
Implicit
ALKNIT
Photolysis
[jalknit->,jch3ooh] ALKNIT + hv -> NO2 + 0.4*CH3CHO + 0.1*CH2O + 0.25*CH3COCH3 + HO2 + 0.8*MEK
Chemical Reactions
[ALKNIT_OH] ALKNIT + OH -> 0.4*CH2O + 0.8*CH3CHO + 0.8*CH3COCH3 + NO2 ; 1.6e-12
[ALKOOH_OH] ALKOOH + OH -> ALKO2 ; 3.8e-12, 200
[tag_CH3CO3_NO2] CH3CO3 + NO2 + M -> PAN + M ; 9.7e-29, 5.6, 9.3e-12, 1.5, 0.6
[usr_PAN_M] PAN + M -> CH3CO3 + NO2 + M
Adding Gas-Phase Chemistry

## Slide 9
  Add unique chemical reaction formats into mo_usrrxt.f90 file.
    CESM is set-up such that code changes are put in a specific folder within your case directory such that accounting for code changes is simple and trackable.
!-----------------------------------------------------------------
! ... pan + m --> ch3co3 + no2 + m (JPL15-10)
!-----------------------------------------------------------------
call comp_exp( exp_fac, -14000._r8*tinv, ncol )
if( usr_PAN_M_ndx > 0 ) then
if( tag_CH3CO3_NO2_ndx > 0 ) then
rxt(:,k,usr_PAN_M_ndx) = rxt(:,k,tag_CH3CO3_NO2_ndx) * 1.111e28_r8 * exp_fac(:)
else
rxt(:,k,usr_PAN_M_ndx) = 0._r8
end if
end if
Adding Gas-Phase Chemistry

## Slide 10: Adding Gas-Phase Chemistry
  Photolysis Reactions
    Photolysis reactions in CESM are derived from a look-up table based on TUV.
    New photolysis reactions can be mapped to a rate in the look-up table with an optional multiplication factor.
[jalknit->,jch3ooh] ALKNIT + hv -> NO2 + 0.4*CH3CHO + 0.1*CH2O + 0.25*CH3COCH3 + HO2 + 0.8*MEK
[jalkooh->,jch3ooh] ALKOOH + hv -> 0.4*CH3CHO + 0.1*CH2O + 0.25*CH3COCH3 + 0.9*HO2 + 0.8*MEK + OH
[jbepomuc->,.10*jno2] BEPOMUC + hv -> BIGALD1 + 1.5*HO2 + 1.5*CO
[jbigald->,0.2*jno2] BIGALD + hv -> 0.45*CO + 0.13*GLYOXAL + 0.56*HO2 + 0.13*CH3CO3 + 0.18*CH3COCHO

## Slide 11: Adding Gas-Phase Chemistry
  Update henry’s law constants that are used for wet/dry deposition in seq_drydep_mod.F90
    There are several arrays containing: 1) species names, 2) reactivity factors (f0), 3) henry's law constants, and 4) molecular weights.
  Update gamma values for gas-phase compound aerosol uptake in mo_usrrxt.f90 file
real(r8), parameter :: gamma_isopnita = 0.005_r8 ! from Fisher et al., ACP, 2016
c_isopnita = 1.20e3_r8 * sqrt_t(i) ! mean molecular speed of isopnita
!-------------------------------------------------------------------------
! ... ISOPNITA -> HNO3 (on tropospheric aerosol surfaces except dust and seasalt)
!-------------------------------------------------------------------------
if( usr_ISOPNITA_aer_ndx > 0 ) then
rxt(i,k,usr_ISOPNITA_aer_ndx) = hetrxtrate( sfc, dm_aer, dg, c_isopnita, gamma_isopnita )
end if

## Slide 12: Adding Gas-Phase Chemistry
  Adjust the namelist to include new tracers. Many changes within CESM can be made through the namelist, which does not require code manipulation or recompiling.
    Output new species
    New species mapping of emissions files
    New species mapping of biogenic emissions from MEGAN
fincl1 = 'CFC11STAR', 'AODDUST', 'AODDUST2', 'T', 'U', 'V', 'O3', 'OH',
'NO3', 'HO2', 'LNO_COL_PROD', 'NO2_CLXF', 'SFNO', 'SFNH3', 'BRO', 'CH3CL’,…
…
'BIGALK -> /glade/p/cesmdata/cseg/inputdata/atm/cam/chem/emis/CMIP6_emissions_1750_2015/emissions-cmip6_BIGALK_anthro_surface_1750-2015_0.9x1.25_c20170608.nc',
'BIGALK -> /glade/p/cesmdata/cseg/inputdata/atm/cam/chem/emis/CMIP6_emissions_1750_2015/emissions-cmip6_BIGALK_bb_surface_1750-2015_0.9x1.25_c20170322.nc’,
…
megan_specifier = 'ISOP = isoprene',
'MTERP = pinene_a + carene_3 + thujene_a + 2met_styrene + cymene_p + cymene_o + terpinolene + bornene + fenchene_a + ocimene_al + pinene_b + sabinene + camphene + limonene + phellandrene_a + terpinene_g + terpinene_a + phellandrene_b + myrcene + ocimene_t_b + ocimene_c_b’,…

## Slide 13: Adjusting VBS Schemes for SOA Formation
[ISOP_NO3_vbs] ISOP + NO3 -> ISOP + NO3 + 0.059024*SOAG3 + 0.025024*SOAG4 ; 3.03e-12, -446
[ISOP_O3_vbs] ISOP + O3 -> ISOP + O3 + 0.0033*SOAG3 ; 1.05e-14, -2000
[ISOP_OH_vbs] ISOP + OH -> ISOP + OH + 0.0031*SOAG0 + 0.0035*SOAG1 + 0.0003*SOAG2 + 0.0271*SOAG3 + 0.0474*SOAG4 ; 2.54e-11, 410
  The VBS chemical scheme is in the same input file as the gas-phase chemical reactions.
  There are 5 volatility bins for oxidized VOCs in the default mechanism (SOAG0, SOAG1, SOAG2, SOAG3, SOAG4).

## Slide 14: Conclusion
We are constantly updating and improving chemistry in CESM and we welcome collaboration.
Comparisons of CESM and GEOS-Chem chemical mechanisms would be beneficial.
Updating/adding gas-phase chemistry and adjusting vbs schemes is relatively easy in CESM.
We have recently created a CAM-Chem wiki to explain how to run CAM-Chem including detailed descriptions of how to update chemistry (https://wiki.ucar.edu/display/camchem/Home)
We can provide guidance and help with errors.

## Slide 15: Extra Slides

## Slide 16: Modal Aerosol Module-4 (MAM4)
(Liu et al., Geosci. Model Dev., 2016)

## Slide 17: Default VBS Scheme
OH
OH, O3, NO3
SVOC
IVOC
OH
SOAG0
SOAG1
SOAG2
SOAG3
SOAG4
Wet/Dry
Deposition
soa1_a1, soa1_a2
soa2_a1, soa2_a2
soa3_a1, soa3_a2
soa4_a1, soa4_a2
soa5_a1, soa5_a2
(Aitken and accumulation)
Secondary Organic Aerosol
Wet/Dry
Deposition
soa1_c1, soa1_c2
soa2_c1, soa2_c2
soa3_c1, soa3_c2
soa4_c1, soa4_c2
soa5_c1, soa5_c2
(in cloud)
hv
Semi-volatile compounds split into Volatility Bins
Partitioning based on Volatility
(Hodzic et al., 2016)