## Slide 1
GEOS-Chem Adjoint Model
07/30/2018
>100 registered users at more than 23 institutions
Daven K. Henze, CU Boulder, Adjoint Model Scientist
Jun Wang, U Iowa, Adjoint and Data Assimilation WG Co-Chair
Yanko Davila, CU Boulder, Adjoint Model Code Support

## Slide 2: An adjoint model...
...efficiently calculates derivatives of a scalar model response with respect to all model parameters (emissions, rate constants, ...)
resolved at the native model resolution.

## Slide 3: An adjoint model...
Contributions to annual Arctic BC column concentrations (Xu et al., 2017)
Source attribution
...efficiently calculates derivatives of a scalar model response with respect to all model parameters (emissions, rate constants, ...)
resolved at the native model resolution. Used for:

## Slide 4: An adjoint model...
Inverse modeling / 4D-Var
Optimization
adjoint:
dJ/dparameters
J ~ [model – obs]2
Parameters
Contributions to annual Arctic BC column concentrations (Xu et al., 2017)
...efficiently calculates derivatives of a scalar model response with respect to all model parameters (emissions, rate constants, ...)
resolved at the native model resolution. Used for:
post
prior
CO emissions constrained using MOPITT (Jiang et al., 2015)
Source attribution

## Slide 5: adjoint code: details
IF ( W > a )
W = Y ** 2
ELSE
W = Y * Z
END
Forward
IF ( W > a)
Y_ADJ = 2 * Y * W_ADJ
ELSE
Y_ADJ = Z * W_ADJ
Z_ADJ = Y * W_ADJ
END
Adjoint
Consider model state vector x = [w,y,z], model M:
Notes: {\bf \lambda}^{k} = \left [ \frac{\partial(M({\bf x}^k))}{\partial {\bf x}^k} \right ]^T {\bf \lambda}^{k+1}

## Slide 6: Potential applications of GC adjoint within NCAR models
CESM2:
  Chemical sensitivity analysis under a range of climates or meteorologies (e.g., global premature moralities/kg NOx emitted in any grid-box under present vs warmer climate)
  4D-Var inverse modeling with state-of-science treatment of non-atm components (land surface, ocean, snow/ice,…)

## Slide 7: Potential applications of GC adjoint within NCAR models
CESM2:
  Chemical sensitivity analysis under a range of climates or meteorologies (e.g., global premature moralities/kg NOx emitted in any grid-box under present vs warmer climate)
  4D-Var inverse modeling with state-of-science treatment of non-atm components (land surface, ocean, snow-ice,…)
CESM2 / WRF: Better characterization of model-error use of different physics for 4D-Var inverse modeling and DA
  Model error is a critical term in inverse modeling and DA
  Can be tuned (Bousserez et al., in prep) or optimized (weak-constraint 4D-Var, Stanevich et al., submitted), which is elegant in theory but difficult in practice.
  Previously w/GEOS-Chem it has been roughly estimated using e.g. GEOS4 vs GEOS5 meteorology
    not a robust ensemble, and GC not supporting older met
    in contrast, with WRF we’ve used 156 model configs to estimate model error contribution to R (Guerrette et al., 2015)
Notes: J({\bf x}) = (H({\bf x}) - {\bf y})^T {\bf R}^{-1} (H({\bf x}) - {\bf y}) + ({\bf x} - {\bf x}_b)^T {\bf B}^{-1} ({\bf x} - {\bf x}_b)

## Slide 8: Potential applications of GC adjoint within NCAR models
WRF-Chem: Hi-resolution regional 4D-Var data-assimilation and inverse modeling (ignoring impacts of chemistry on dynamics)
  Would need to implement driver for running in reverse (sensitivity analysis) and solver for inversion/DA

## Slide 9: Adjoint model within an inverse model
Inverse Model
Forward Model
t0
tf
Parameter Estimate
Predictions,
Optimization
(L-BFGS)
Improved
Estimate
y = observations, B,R = uncertainties
Adjoint Forcing,
Gradients
(sensitivities)
Adjoint Model
tf
t0

## Slide 10: Potential applications of GC adjoint within NCAR models
WRF-Chem: Hi-resolution regional 4D-Var data-assimilation and inverse modeling (ignoring impacts of chemistry on dynamics)
  Would need to implement driver for running in reverse (sensitivity analysis) and solver for inversion/DA
WRFPLUS-Chem, WRFDA-Chem [Guerrette & Henze 2015; 2017]: DA and inverse modeling that accounts for feedback of chemistry on dynamic (or chem as a tracer for dynamics)
  expand beyond current state (just GOCART aerosols and sulfate chemistry)
    Full chemistry
    Inert GHGs
Other?

## Slide 11: How adjoint code is made
Adjoint models can be made in several ways:
Application of automatic differentiation algorithms to forward model code
  TAPENADE: widely used generic tool
Manually applying the algorithms embedded in AD software to the forward model source code line-by-line
  Can generate code that is sleeker than AD-generated
Deriving the adjoint of discrete numerical algorithms
  This is how the KPP-generated adjoint works for chemistry
Deriving the adjoint of the continuous physics equations, and then discretize and solve these
  This is how the adjoint works for xy transport
 Any modification to the forward model requires a commensurate update to the adjoint code

## Slide 12: An adjoint model...
...runs “backwards” in time
From a software engineering standpoint, this means that the forward model needs to be able to be run in reverse time.
Adjoint model can be somewhat invasive to the forward model, as this may require changes to the standard forward model driver
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 13: GEOS-Chem adjoint model
- adjoint model is a separate code, with separate code versions
- single exec for forward model, adjoint model, and DA solver (pros and cons of this approach), iterations with shell script
- based on the forward model code with periodic updates, patches, and major overhalls (from v5 to v6, to v7, to v8… now working on v11 / GCHP)
- code managed through gitlab hosted at adjoint.colorado.edu
- adjoint model code support from Yanko Davila
- community model w/policies and procudures for updating similar to GEOS-Chem forward model

## Slide 14: Adjoint code updates
Chart: GCADJ version 35 commit dates
| 41479.0 | 41577.0 | 41662.0 | 41740.0 | 41830.0 | 41871.0 | 42089.0 | 42157.0 | 42171.0 | 42296.0 | 42476.0 | 42845.0
version | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Code update cycle
Adjoint models often lag forward models
Sometimes that is ok or even preferable for DA, for which adjoint is often simpler / coarser than full forward model (e.g., operational NWP centers)

## Slide 15: GEOS-Chem adjoint code status (v35m)
From v8-02-1 forward model code base
adjoint of all code excluding:
  SOA, aerosol microphysics packages
  non-local PBL mixing
  GEOS-FP / MERRA2 convection
pulled all model updates and bug fixes up through v10
  excluding those that pertain to non-supported parts of the forward code
Fullchem, gly-chem, UCX, plus offline simulations for CH4, CO2, N2O, BC, dust, CO
Implemented features not yet standardized in forward model
  N2O
  NH3 bidirectional exchange and diurnal variability

## Slide 16: Adjoint code benchmarking
Inverse modeling test using psuedo observations (i.e. an inversion where ”observations” are based on a model simulation with known emissions)
Sensitivity test (default d(Ox)/d(NOx)) through comparison of finite difference to adjoint sensitivities (w/xy-transport disabled)
Results from each version published on wiki
These tests are valuable but not exhaustive
  Puedo inversions and FD tests are built-in simulation modes that can be used by any user
Notes: ]

## Slide 17
Validating code (IDL/matlab scripts provided)
Adjoint
Finite Difference

## Slide 18: How adjoint code is made: checkpointing
Storage of forward model variables to disk or in memory for use within the adjoint (i.e., checkpointing) required at code junctures and nonlinearities
IF ( W > a )
W = Y ** 2
ELSE
W = Y * Z
END
IF ( W > a)
Y_ADJ = 2 * Y * W_ADJ
ELSE
Y_ADJ = Z * W_ADJ
Z_ADJ = Y * W_ADJ
END
Forward
Adjoint
Note: checkpointing requires altering the forward model
Notes: {\bf \lambda}^{k} = \left [ \frac{\partial(M({\bf x}^k))}{\partial {\bf x}^k} \right ]^T {\bf \lambda}^{k+1}

## Slide 19: Checkpionting details
Guerrette & Henze, 2015
∆t chem,external
∆t chem, KPP, internal
Checkpt
Checkpt

## Slide 20: Adjoint model: hardware requirements
Requirements:
- checkpointing: data written during fwd, read during adjoint
- forward model slower than standard owing to heavy i/o
- memory usage ~x4 of standard forward model
- adjoint requires x2-4 of standard forward CPU time
Examples (on dual hex-core Xeon 2.6 GHz):
- fwd+adj full chem, global 2x2.5, 1 month
- 400 GB checkpoint files
- 30 hours w/busy NFS scratch
- 9 hrs w/local SS scratch
- fwd+adj of offline CO2, global 2x2.5, 1 month
- 2.5 GB checkpoint files
- 2 hours

## Slide 21: GEOS-Chem adjoint future
Updating to use GCHP and HEMCO the current development challenges
  Starting w/CO2 simulation, for which the adjoint is trivial
  Challenge is running GCHP in reverse time
Incorporation into online models
  WRFPLUS-Chem
  GEOS-5 has an adjoint
Incorporation into generic DA toolkits being championed by NWP community
  JEDI
  OOPS

## Slide 22: Find out more…
Visit us at:
http://wiki.seas.harvard.edu/geos-chem/index.php/GEOS-Chem_Adjoint (wiki)
- manuals, instructions, publications
- code features
- current version overviews
- benchmarks
http://adjoint.colorado.edu:8080 (code GitLab)
- code distribution
https://trello.com/b/GTfHT38L/geos-chem-adjoint (pipeline)
- code development cycle / pipeline
GEOS-Chem adjoint code support:
- yanko.davila@colorado.edu

## Slide 23: extra slides
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 24: Adjoint model: current and new features
Standardized code: v35l, maintained / distributed via GIT
Code base : v8-02-01 with relevant fixes / updates up to v10
Meteorology: GEOS-4, GEOS-5, GEOS-FP, MERRA2
Simulations : full chem; gly-chem, offline CO, Ox, CO2, CH4, BC, Dust, N2O
Resolution : 4x5, 2x2.5, 0.5 x 0.667, 0.25 x 0.3125
Processes: all main forward model process excluding:
- non-local pbl mixing scheme
- aerosol microphysics
- feedback of aerosols on photolysis or heterogeneous chemistry
- UCX (in progress), HEMCO
Species: forward full chemistry model species excluding:
- SOA, SO4s, NITs, Br
Model update cycle slowed while waiting for GCHP / FlexChem…
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 25: Adjoint model: tracking activities
See GC adjoint wiki page, GitLab and Trello for details:
Benchmarking: finite difference vs adjoint
http://wiki.seas.harvard.edu/geos-chem/index.php/GEOS-Chem_Adjoint (wiki)
http://adjoint.colorado.edu:8080 (code GitLab)
https://trello.com/b/GTfHT38L/geos-chem-adjoint (pipeline)
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 26: WRFPLUS-Chem
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 27: Discrete adjoint code example
Forward Run
Adjoint Run
Let

## Slide 28: An adjoint model...
...efficiently calculates gradients of a scalar model response with respect to all model parameters (emissions, rate constants, ...)
at the native model resolution.
Sensitivity of all model concentrations to one model source
Perturbation at source region at t0
Forward
Changes of concentration at tn
Forward Model (source-oriented)
cost scales with # of sources
Sensitivity of model concentration in specific location to many model sources
Adjoint Model (receptor-oriented)
Concentration at the receptor at tn
cost scales with # of receptors
adjoint
area of
possible origin at t0
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 29: Recent and current applications: Source attribution
Climate
- Aerosol Radiative forcing and Temperature (Lacey, CU Boulder)
- Ozone and CH4 RF (Walker, JPL)
- CCN (Capps, Drexel)
- BC in the Arctic (Qi, UCLA; Xu, Dalhousie)
Air quality
- Background O3 (JPL)
- PM2.5 source attribution (Zhang, Peking)
- PM2.5 health impacts (Dedoussi, MIT; Zhang, Tsinghua; Lee, Dalhousie; Lacey, CU Boulder; Koplitz, Harvard)
- O3 health impacts (Henze, CU Boulder)
- NOx sensitivity to emissions (Bowman, JPL)
- GC adjoint vs HTAP multi-model source-receptor relationships (Davila, Henze, CU Boulder)
Ecosystem impacts
O3 vegetative exposure and crop loss (Lapina, CU Boulder)
N deposition (Lee, CU Boulder; Zhao, Peking)
Blue = person presenting this topic at IGC8
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 30: Recent and current applications: 4D-Var inverse modeling and data assimilation
Aerosol and aerosol precursor emissions
- Aerosol with MODIS, CALIPSO (Wang, UI; Lee, Dalhousie; Chen, CNRS)
- NH3 with TES (Zhang, Peking)
- SO2 and NO2 with OMI (Wang, UI; Qu, CU Boulder; Cooper, Dalhousie)
Greenhouse gases
- CH4 (Turner, Harvard/UCB; Bousserez, CU Boulder; Stanevich, UT; Tan, Purdue)
- CO2 (Liu, Lee, Bowman, JPL; Deng, Jones, UT)
- N2O (Wells, U. Minnesota)
Reactive gas-phase species
- CO from MOPITT (He, UT)
- Isoprene from OMI HCHO (Kaiser, Harvard)
- NMVOCs (Cao, Peking U.)
- CO, NO2 and O3 (Miyazaki, JAMSTEC/JPL; Zhang, UT)
Method advancement and comparisons
- Weak constraint 4D-Var (He, Stanevich, UT)
- UQ and model reduction (Bousserez, CU Boulder)
- Grid-scale vs optimal aggregation (Turner, Harvard;
Wells, U Minn)
- 4D-Var and EnKF (Miyazaki, JAMSTEC/JPL; Liu, JPL)
- Mass balance vs 4D-Var (Qu, CU Boulder; Cooper, Dalhousie)
- Verification of top-down CO2 flux constraints (Liu, JPL)
Satellite design
- GEO-CAPE (Bousserez; CU Boulder)
- CLARREO (Wang, UI)
Kaminski & Heimann, 2001
Peylin et al., 2001
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 31
Adjoint sensitivities
Finite Difference sensitivities
m = 0.993
R2 = 0.998
2nd order (centered) FD = J(s+0.1) – J(s-0.1) / 0.2
1st order (+10%) FD = J(s+0.1)/J(s)
1st order (-10%) FD = J(s-0.1)/J(s)

## Slide 33: Adjoint Application on PM2.5 pollution over China - Data Assimilation and Source Attribution
The CNEMC Monitoring Sites
Emissions
The GEOS-Chem Model and its Adjoint
Prior Simulation
Optimized Simulation
Improved Source Attribution
Data Assimilation
Forward Model
Optimized Model
Adjoint Sensitivity
L. Zhang, et al., Sources and Processes Affecting Fine Particulate Matter Pollution over North China: An Adjoint Analysis of the Beijing APEC Period, ES&T, 2016.

## Slide 34: GEOS-Chem adjoint major new directions: health impacts and integrated assessment
(e.g., Dedoussi, MIT; J. Lin and Q. Zhang, Peking/Tsinghua, Baublitz, Columbia; Henderson, EPA; Henze and Lacey, CUB)
Response
∆O3,
∆PM2.5
∆CH4
Benefits
- health
- climate
- crop yield
Mitigation
∆Emissions
LEAP-IBC: rapid emission and scenario assessment toolkit for UNEP
Zhao et al., ACPD, 2017
Koplitz et al., ERL, 2016
Impacts of atm transport vs trade on PM2.5 mortality in China
e.g. Lacey et al., PNAS, 2017
Notes: RF(NO_x) = \frac{\partial RE(O_3)}{\partial NO_x} + \frac{\partial RE(CH_4)}{\partial NO_x} + \frac{\partial RE(PM)}{\partial NOx}+\dots

## Slide 35
Code flowchart (Meemong Lee)

## Slide 38
Adjoint clinic slides